## Slide 1: Mobile IPv6 趨勢介紹

## Slide 2: Mobile IP and its Variants
Mobile IPv4 (MIPv4)
  MIPv4
  Low-Latency Handover for MIPv4 (FMIPv4)
  Regional Registration for MIPv4 (HMIPv4)
Mobile IPv6 (MIPv6)
  MIPv6
  Fast Handover for MIPv6 (FMIPv6)
  Hierarchical MIPv6 (HMIPv6)

## Slide 3: MIPv4: Overview
MIPv4 Nodes
  MN (Mobile Node): Host
  CN (Correspondent Node): Host
  HA (Home Agent): Router
  FA (Foreign Agent): Router
MIPv4 Address
  HoA (Home Address): MN
  CoA (Care-of-Address): FA

## Slide 4: Home Address (HoA) and Care-of Address (CoA)

## Slide 5: MIPv4 Agents
Home Agent (HA) & Foreign Agent (FA)

## Slide 6: MIPv4: Control Operations
Agent Discovery
  MN  FA (CoA)
  ICMP Agent Solicitation & Advertisement
Registration to HA (via FA)
  MN  FA  HA
  Over UDP (destination port 434)
Data Tunneling
  CN => HA (HoA) => FA (CoA) => MN
  IP-in-IP Tunneling, ..

## Slide 7: MIPv4: Control & Data Flows

## Slide 8: Mobile IPv6 (MIPv6)
MIPv6 = MIPv4 + IPv6
Major Differences from MIPv4
  FA in MN
    No FA for MIPv6
  CoA: IP address of MN
    By DHCPv6 or IPv6 Stateless Auto-Configuration
  Route Optimization
    To solve the “Triangular Routing” Problem
    Provided by default
    MN  CN

## Slide 9: MIP: Triangular Routing Problem

## Slide 10: MIPv6: Route Optimization

## Slide 11: MIPv6: Binding Update
Binding Update to HA
  Using IPSEC: MN and HA have a security association
    AH (Authentication Header)
    ESP (Encapsulating Security Payload)
Binding Update to CN
  Return Routability (RR) procedure
    For Security
  Binding Update (BU) procedure
    Route Optimization

## Slide 12: MIPv6: Binding Update (Cont.)

## Slide 13: MIPv6: RR (Return Routability)

## Slide 14: MIPv6: Changes to IPv6
New IPv6 Protocol (Header)
  Mobility Header: a new IPv6 extension header
    To carry MIPv6 Binding Update messages
    How is in the MIPv4 ?
  New Option in Destination Option Header
    Home Address Option
  New Type in Routing Header
    Type 2 Routing Header
New ICMP Messages
  ICMP HA Address Discovery Request/Reply
  ICMP Mobile Prefix Solicitation/ Advertisement

## Slide 15: References
Mobile IP